## Slide 1: A Modem Testbed for Body Area Network (BAN) Communication
Internship wrap-up presentation
      Yifang Chen
Mentor: Brian Taff
8-Aug-2017
Feb 9th, 2017
BIOTRONIK // CRM

## Slide 2: The present cardiac rhythm management (CRM) market
Traditional canned devices
    Generator implanted in chest
      Substantial scarring/bulge
    Transvenous lead connections to heart
      Infection risk
    Extensive testing/design for MRI safety
Leadless pacing
    Catheter-based implantation
      No chest scar
    Device implanted within heart
      Minimized infection risk
    Inherently MRI safe
The future
Notes: 60

## Slide 3: The value of BAN communication in CRM products
Multi-chamber leadless
    Beat-by-beat communication
      Few bits, sent often
    Enables synchronization of atrium and ventricle
      More physiologic heart function
Atrium
Ventricle
BAN
Home monitoring (HMSC)
Sub-Q hub
(BM)
    Leadless pacer stats relayed to web
      Many bits, sent daily
    Subcutaneous hub powers RF relay
      Returns core canned
      device functionality
Anti-tachycardia pacing (ATP)
    Extends capabilities of new-generation defibrillators
      Few bits, sent rarely
    Less painful, low power means for halting some fatal rhythms
BAN
RF
GSM
Shock box
Leadless pacer
BAN
(Please pace)
Notes: 60

## Slide 4
Motivation:
In order to assess the BAN communication for iLPs, under:
the different SW modem design templates, and
the different physical-layer infrastructures,
a new, configurable system, which is hardware-platform independent, is needed.
Software-defined Radio Bench Modems
Transmitter
Receiver
Galvanic
Acoustic
Data
Data
OR
Digital
Analog
Acoustic
Galvanic
Physical-layer test environment
Project Overview
Notes: 90s

## Slide 5
Software-defined Radio Bench Modems
Transmitter
Receiver
Galvanic
Acoustic
Data
Data
OR
Digital
Analog
Acoustic
Galvanic
Physical-layer test environment
Project Overview
Presentation outline:
Develop library of SW-defined radio modems
Build infrastructure for physical-layer testing
Collect test result
Summary and Possible Project Extension
Notes: 90s

## Slide 6
Outline:
Develop library of SW-defined radio modems
Build infrastructure for physical-layer testing
Collect test result
Summary and Possible Project Extension
Software-defined Radio Bench Modems
Transmitter
Receiver
Galvanic
Acoustic
Data
Data
OR
Digital
Analog
Acoustic
Galvanic
Physical-layer test environment
Project Overview
Notes: 90s

## Slide 7
Packet Encoder/Decoder
    A translator between human language and computer language
    text   binary digits
Interface to Transmitter/Receiver
    Tell the transmitter/receiver how I want to send/receive the modulated signal
Signal Modulation/Demodulation
    A translator between computer language and physical world language
    binary digits   physical wave
The targeted text message
Access code
‘hello
world’
Code to indicate the beginning of packet
10101100…001 (varies)
01001000 01100101 01101100 01101100 01101111 01110111 01101111 01110010 01101100 01100100
ASK:
Amplitude shift
FSK:
Frequency shift
PSK:
Phase
shift
…
Tx
Tx
Rx
Rx
Develop library of SW-defined radio modems
Notes: 90s:
1\why we need to develop a system?
2\workflow

## Slide 8
ASK
FSK
PSK
Frequency Shift Key:
Good noise immunity
More bandwidth efficient
More complex design than ASK
0
1
Phase Shift Key:
Good noise immunity
Slightly more bandwidth efficient
More complex design than FSK
More Power Consumption
Amplitude Shift Key:
Bad noise immunity
Less bandwidth efficient
Simple design
1
0
0
1
Time Domain
Constellation Domain
Frequency Domain
Frequency Domain
Frequency Domain
------------------------- binary digits 1,0
------------------------- modulated signal
25KHz
35KHz
Time Domain
Notes: 60s

## Slide 9
Modulation (TX)
De-modulation (RX)
A deeper look into FSK
Notes: 60s

## Slide 10
Modulation(TX)
De-modulation (RX)
A deeper look into FSK
Notes: Picture need to change; need VCO?

## Slide 11
Modulation
De-modulation (RX)
Message interval: only noise
Message interval: only noise
Receiver NOT prepared for sudden jump from noise to message
Fill empty interval with 101010… preamble sequence
Access code + “helloworld”
Receiver prepared for receiving targeted message by 1010…
Message interval: only noise
Message interval: only noise
A deeper look into FSK
Notes: 30s

## Slide 12
Modulation(TX)
De-modulation (RX)
A deeper look into FSK
Notes: Picture need to change; need VCO?

## Slide 13
‘0’  25kHz
‘1’  35KHz
Modulation(TX)
De-modulation (RX)
A deeper look into FSK
Notes: Picture need to change; need VCO?

## Slide 14
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Modulation(TX)
De-modulation (RX)
A deeper look into FSK
Notes: 30s

## Slide 15
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Modulation
De-modulation (RX)
Voltage Controlled Oscilloscope:
(1) Generate Cosine Waves; (2) Control its frequency using input voltage
Signal with 25K (0) and 35K (1) volts
25000
35000
…
Amplitude
1
0.5
0
-0.5
-1
Amplitude
A deeper look into FSK
Notes: 30s

## Slide 16
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Modulation(TX)
De-modulation (RX)
A deeper look into FSK
Notes: 30s

## Slide 17
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Modulation(TX)
De-modulation (RX)
A deeper look into FSK
Notes: Picture need to change; need VCO?

## Slide 18
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Modulation
De-modulation
0
1
DC offset (don’t matter)
Filtered out the high frequency noise
(for better understand, here I use frequency domain instead od time domain before)
noise
noise
Down-sampling: /200
Received Signal in Frequency Domain
Low passed signal in Frequency Domain
A deeper look into FSK
Notes: 30s

## Slide 19
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Down-sampling:
/100
Modulation(TX)
De-modulation (RX)
A deeper look into FSK

## Slide 20
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Down-sampling:
/100
Modulation
De-modulation
35KHz ->positive value (1); 25KHz ->negative value (0);
0
1
DC offset (don’t matter)
Low passed signal in Frequency Domain
Recovered Signal in Time Domain
Example here is 1,0,1,0,… signal sequence
A deeper look into FSK
Notes: 30s

## Slide 21
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Modulation(TX)
De-modulation (RX)
Down-sampling:
/100
A Deeper Look into FSK
Notes: Picture need to change; need VCO?

## Slide 22: A Deeper Look into FSK
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Up-sampling:
/200
‘0’  25kHz*2pi; ‘1’  35KHz*2pi
Modulation
De-modulation
    22
(1)Down-sample again:/2 to recover the original symbol rate
(2) Further Smooth the signal
Example here is 1,0,1,0,… signal sequence
Recovered Signal in Time Domain
Further Recovered Signal in Time Domain
Notes: Picture need to change; need VCO?

## Slide 23: A Deeper Look into FSK
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Modulation(TX)
De-modulation (RX)
Up-sampling:
/200

## Slide 24: A Deeper Look into FSK
Up-sampling:
Repeat each symbol X 200 times
‘0’  25kHz
‘1’  35KHz
Up-sampling:
/200
/ 2
Modulation
De-modulation
    24
Truncate float to Binary:
positive 1; negative 0
Example here is 1,0,1,0,… signal sequence
1
0
Notes: 20-23: 30s

## Slide 25
Software-defined Radio Bench Modems
Transmitter
Receiver
Galvanic
Acoustic
Data
Data
OR
Digital
Analog
Acoustic
Galvanic
Physical-layer test environment
Project overview
Presentation outline:
Develop library of SW-defined radio modems
Build infrastructure for physical-layer testing
Collect test result
Summary and Possible Project Extension
Notes: 90s

## Slide 26
Software-defined Radio Bench Modems
Transmitter
Receiver
Galvanic
Acoustic
Data
Data
OR
Digital
Analog
Acoustic
Galvanic
Physical-layer test environment
Project overview
Presentation outline:
Develop library of SW-defined radio modems
Build infrastructure for physical-layer testing
Collect test result
Summary and Possible Project Extension
Notes: 90s

## Slide 27
  Distance: 40mm – 200 mm
  Orientation:
Right Atrium (RA)
Right Ventricle (RV)
BM chest
S-ICD
~70mm
Right Ventricle (RV)
~140mm
Right Atrium (RA)
Or
Right Ventricle (RV)
Right Atrium (RA)
Or
~130mm
Skin Simulation: Anechoic chamber (container surrounded by anechoic foam)
Body Fluid Simulation:
Saline concentration = 2.0g/L; Conductivity 2.85mS/cm
Air in lungs Simulation:
Using Balloon
only needed in S-ICD case
salt
BAN Testing Parameters:
  Transmission Media:
Physical testing environment
Notes: 90s

## Slide 28
Device positioning fixture:
Enables stable device positioning
Actual use in saline tank
Physical testing environment

## Slide 29
Software-defined Radio Bench Modems
Transmitter
Receiver
Galvanic
Acoustic
Data
Data
OR
Digital
Analog
Acoustic
Galvanic
Physical-layer test environment
Project overview
Presentation outline:
Develop library of SW-defined radio modems
Build infrastructure for physical-layer testing
Collect test result
Summary and Possible Project Extension
Notes: 90s

## Slide 30
Software-defined Radio Bench Modems
Transmitter
Receiver
Galvanic
Acoustic
Data
Data
OR
Digital
Analog
Acoustic
Galvanic
Physical-layer test environment
Project overview
Presentation outline:
Develop library of SW-defined radio modems
Build infrastructure for physical-layer testing
Collect test result
Summary and Possible Project Extension
Notes: 90s

## Slide 31
Rx/Tx iLP
Orientation
Distance
Acoustic
Galvanic
Parallel
Cross
Face-to-face
100mm
Modulation Methods
Total Required Bandwidth
20KHz
FSK
Noise
No noise
Noise (f = carrier + 9KHz)
HW Factors
SW/Algorithm-factors
Environmental Factors
Accuracy:
1 Byte Message
10 Byte Message
Parameter Scope
Testing Values
Parameters
1.Received packet percentage
2.Bit Error Rate (BER) of received packets
3.Estimated total Bit Error Rate
Outline for testing dual-chamber use case
Notes: 60s

## Slide 32: Testing Result – Screenshot example
Original Signal VS Demodulated Signal
“Hello World!”
“H@llo Werld!”
RX
TX
Bit Error Rate ~= 35%
Notes: 30s

## Slide 33
How does noise influence accuracy?
BER rises exponentially with increasing noise – for a fixed distance, location, and packet size
~200mV = max. permissible noise voltage for 1990KHz signal (signal amplitude ~= 1.54V)
Noise voltage (mV)
Bit Error Rate
Preliminary test results using a galvanic physical layer
Notes: 90s:
1\why we need to develop a system?
2\workflow

## Slide 34: Testing Result – Parameters that influence Galvanic Accuracy
How orientation influence accuracy? (each series corresponds to a unique distance)
For face-to-face orientation, larger distance will give more accurate transmission at least in range around 100mm
-----: smaller distance (use middle as reference point)
-----: larger distance (use head as reference point)
Bit Error Rate
Noise voltage (mV)
Face-to-Face Orientation
Noise voltage (mV)
Cross Orientation
Notes: 90s:
1\why we need to develop a system?
2\workflow

## Slide 35
How does orientation influence accuracy?(each series corresponds to each orientation)
General trend for improved data transception: Parallel > Face-to-face > Cross
-----: Face-to-Face
-----: Parallel
Bit Error Rate
Noise voltage (mV)
-----: Cross
Preliminary test results using a galvanic physical layer
Notes: 90s:
1\why we need to develop a system?
2\workflow

## Slide 36
Provided SDD with a new configurable tool for assessing BAN modem design templates and performing comparative testing of physical layer communication technologies
  Includes code (SW in GNU radio) that is readily portable to more mature test hardware (i.e. National Instruments vs. HackOne RF)
  Interfaces with a saline test environment capable of mimicking a multitude of BAN communication use cases
Begin preliminary testing that should ultimately facilitate the first “apples to apples” comparisons of in-house SDD physical layer communication methodologies
Documented my development and design efforts to enable support for continued system-level benchmarking after my tenure
Summary
Notes: 30s

## Slide 37
  Further improve the assessment system
    Develop additional modulation templates inclusive of PPM
    Transform the high-level SDR system into FPGA language to better assess Tx/Rx efficiencies
    Transition targeted design blocks to analog implementations to better mimic envisionable implant module embodiments
Collecting more testing data
    Explore full suite of developed modem formats and their impact on Tx/Rx accuracy
    Obtain better insight on the role that distance and orientation play
    Extract power efficiency metrics to shed light on design trade-offs
Possible project extensions